## Slide 1: Kismet: Parallel Speedup Estimates for Serial Programs
Donghwan Jeon, Saturnino Garcia, Chris Louie, and Michael Bedford Taylor
Computer Science and Engineering
University of California, San Diego
Attain Their Inner Speedup
Helping Serial Programs
Notes: Hi, my name is Donghwan Jeon.
I am going to present Kismet, parallel speedup estimates for serial programs.
This work is done with my colleagues Sat and Chris, and with my advisor Michael Taylor.

## Slide 2: Questions in Parallel Software Engineering
I heard about these new-fangled multicore chips. How much faster will PowerPoint be with 128 cores?
We wasted 3 months for 0.5% parallel speedup.
Can’t we get parallel performance estimates earlier?
How can I set the parallel performance goals for my intern, Asok?
Dilbert asked me to achieve 128X speedup. How can I convince him it is impossible without changing the algorithm?
Notes: As multi-core processors enter the mainstream computing, there is increasing interest in parallelization.
Let’s look at the types of questions people are asking about parallelization in a hypothetical company that might be familiar to you.
The boss might say with excitement: “…”
But the project manager is skeptical about parallelization: “…”
The Senior engineer, Dilbert, is wondering how he can set the performance target for his intern.
Finally, our intern Asok – we know interns are the smartest in any company – is asked to achieve 128X speedup.But since he is smart, he knows it is impossible without changing the core algorithm,
But he does not know how to convince his boss.
These questions are pretty common because parallelization is often challenging and time-consuming, but the benefit is unpredictable.

## Slide 3: Kismet Helps Answer These Questions
$> make CC=kismet-cc
$> $(PROGRAM) $(INPUT)
$> kismet –opteron -openmp
Cores 1 2 4 8 16 32
Speedup 1 2 3.8 3.8 3.8 3.8
(est.)
1. Produce instrumented binary with kismet-cc
2. Perform parallelism profiling with a sample input
3. Estimate speedup under given constraints
Kismet automatically provides the estimated parallel speedup upperbound from serial source code.
Kismet’s easy-to-use usage model
Notes: Make bottom box a little bit bigger
This is exactly what Dilbert and Asok need to use.

## Slide 4: Kismet Overview
Serial Source Code
Parallelization Planner
Kismet
Sample Input
Parallelization Constraints
Speedup Estimates
Parallelism
Profile
Hierarchical Critical Path Analysis
Kismet extends critical path analysis to incorporate the constraints that affect real-world speedup.
Find the best
parallelization for the target machine
Measure
parallelism
Notes: This figure overviews Kismet system.
As we saw in the usage model of Kismet,
Kismet accepts serial source code and sample input, then profiles the parallelism from the serial execution of the program.
Once the parallelism profile is available,
Parkour’s parallelization planner incorporates other considerations – exploitability, overhead, and resource constraints,
and then reports the speedup estimates.
Parkour extends critical path analysis
to incorporate other key considerations in parallelization.

## Slide 5: Outline
Introduction
  Background: Critical Path Analysis
  How Kismet Works
Experimental Results
Conclusion
Notes: 12:45
Now I’m going to talk about critical path analysis which Parkour extends,
and then show how parkour works with an example,
and then present the experimental results.
Let’s examine critical path analysis.

## Slide 6: The Promise of Critical Path Analysis (CPA)
Definition: program analysis that computes the longest dependence chain in the dynamic execution of a serial program
Typical Use: approximate the upperbound on parallel speedup without parallelizing the code
Assumes: an ideal execution environment
  All parallelism exploitable
  Unlimited cores
  Zero parallelization overhead

## Slide 7: How Does CPA Compute Critical Path?
la $2, $ADDR
load $3, $2(0)
addi $4, $2, #4
store $4, $2(4)
store $3, $2(8)
Notes: Show equation first and show the parallelism number 2.6

## Slide 8: How Does CPA Compute Critical Path?
1
4
node: dynamic instruction with latency
1
la $2, $ADDR
load $3, $2(0)
addi $4, $2, #4
store $4, $2(4)
1
store $3, $2(8)
1
Notes: Show equation first and show the parallelism number 2.6

## Slide 9: How Does CPA Compute Critical Path?
1
4
node: dynamic instruction with latency
edge: dependence between instructions
1
la $2, $ADDR
load $3, $2(0)
addi $4, $2, #4
store $4, $2(4)
1
store $3, $2(8)
1
Notes: Show equation first and show the parallelism number 2.6

## Slide 10: How Does CPA Compute Critical Path?
1
4
work = 8
node: dynamic instruction with latency
edge: dependence between instructions
work: serial execution time, total sum of node weights
1
la $2, $ADDR
load $3, $2(0)
addi $4, $2, #4
store $4, $2(4)
1
store $3, $2(8)
1
Notes: Show equation first and show the parallelism number 2.6

## Slide 11: How Does CPA Compute Critical Path?
1
4
work = 8
node: dynamic instruction with latency
edge: dependence between instructions
critical path length (cp): minimum parallel execution time
work: serial execution time, total sum of node weights
cp = 6
1
la $2, $ADDR
load $3, $2(0)
addi $4, $2, #4
store $4, $2(4)
1
store $3, $2(8)
1
Notes: Show equation first and show the parallelism number 2.6

## Slide 12: How Does CPA Compute Critical Path?
1
4
work = 8
node: dynamic instruction with latency
edge: dependence between instructions
critical path length (cp): minimum parallel execution time
work: serial execution time, total sum of node weights
Total-Parallelism =
work
critical path length
cp = 6
1
la $2, $ADDR
load $3, $2(0)
addi $4, $2, #4
store $4, $2(4)
1
store $3, $2(8)
1
Total-Parallelism
= 1.33
Notes: Show equation first and show the parallelism number 2.6

## Slide 13
All the work on the critical path
Most work
off the critical path
Total-Parallelism
Min 1.0
Totally Serial
……
……
Total-Parallelism Metric: Captures the Ideal Speedup of a Program
Highly Parallel
Notes: What does parallelism metric mean?
It captures the ideal speedup of a program.
As it represents speedup, the minimum value is 1.0.
A program with parallelism 1.0 looks like a long chain
Where all the work is on the critical path of the graph.
When a program’s parallelism is high, the graph looks very different.
It is fat and most work is off the critical path.

## Slide 14: Why CPA is a Good Thing
Works on original, unmodified serial programs
Provides an approximate upperbound in speedup, after applying typical parallelization transformations
  e.g. loop interchange, loop fusion, index-set splitting, …
Output is invariant of serial expression of program
  Reordering of two independent statements does not change parallelism
Notes: Let me tell you why CPA is a good thing.

## Slide 15: A Brief History of CPA
Employed to Characterize Parallelism in Research
  COMET [Kumar ‘88]: Fortran statement level
  Paragraph [Austin ‘92]: Instruction level
  Limit studies for ILP-exploiting processors [Wall, Lam ‘92]
Not widely used in programmer-facing parallelization tools
Notes: Due to those advantages, CPA has been employed in many research project since 1980’s.

## Slide 16: Why isn’t CPA commonly used in programmer-facing tools?
Benchmark
ep
life
is
sp
unstruct
sha
Measured Speedup (16 cores)
15.0
12.6
4.4
4.0
3.1
2.1
Optimism Ratio
648
9228
295503
47482
1112
2.3
Optimism
Ratio
CPA estimated speedups do not
correlate with real-world speedups.
CPA Estimated Speedup
9722
116278
1300216
189928
3447
4.8
Notes: Show measured speedup first, then CPA results
Sort benchmarks to make the point clearer

## Slide 17: CPA Problem #1: Data-flow Style Execution Model Is Unrealistic
void outer( )
{
….
middle();
}
void middle( )
{
….
inner();
}
void inner( )
{
….
parallel doall for-loop
reduction
}
Difficult to map this onto von Neumann machine and imperative programming language
Time
Invoke middle
Invoke inner
Notes: Problem with CPA, not problem of CPA
Top -> outer
Do not use “moment”, use “point” to describe the dotted lines
Revise the slide title

## Slide 18: CPA Problem #2: Key Parallelization Constraints Are Ignored
Overhead
Exploitability
What type of parallelism is supported by the target platform?
e.g. Thread Level (TLP), Data Level (DLP), Instruction Level (ILP)
How many cores are available for parallelization?
Resource Constraints
Do overheads eclipse the benefit of the parallelism? e.g. scheduling, communication, synchronization
Notes: Revise title
“the key parallelization”
“the overhead”

## Slide 19: Outline
Introduction
  Background: Critical Path Analysis
  How Kismet Works
Experimental Results
Conclusion
Notes: 12:45
Now I’m going to talk about critical path analysis which Parkour extends,
and then show how parkour works with an example,
and then present the challenges in Parkour.
Let’s examine critical path analysis.

## Slide 20: Kismet Extends CPA to Provide Practical Speedup Estimates
Parallelization Planner
Kismet
Hierarchical Critical Path Analysis
CPA
Measure parallelism
with a hierarchical region model
Find the best parallelization strategy with target constraints
Notes: 11:59
As we saw in the previous slide,
CPA’s speedup estimation is overly optimistic.
Although CPA incorporates parallelism,
It does not incorporates other key considerations,
and it results in optimistic speedup estimates.
Kismet Extends CPA with key parallelization constraints.
Its hierarchical critical path analysis incorporates parallelism, and parallelization planner takes other constraints into consideration,
achieving more accurate speedup estimation.

## Slide 21: Revisiting CPA Problem #1: Data-flow Style Execution Model Is Unrealistic
void top( )
{
….
middle();
}
void middle( )
{
….
inner();
}
void inner( )
{
….
parallel doall for-loop
reduction
}
Time
Notes: Remove box
Make the text

## Slide 22: Hierarchical Critical Path Analysis (HCPA)
Step 1. Model a program execution with hierarchical regions
Step 2. Recursively apply CPA to each nested region
Step 3. Quantify self-parallelism
loop i
loop j
loop k
foo()
bar1()
bar2()
for (j=0 to 32)
for (i=0 to 4)
for (k=0 to 2)
foo ();
bar1();
bar2();
HCPA Step 1. Hierarchical Region Modeling
Notes: Why functions and loops? Programmer centric units
Let’s examine Hierarchical Critical Path Analysis, or HCPA.
HCPA models the execution of a program with hierarchical regions,
Capturing hierarchical program structure such as loops and functions.
Each region works as a unit of parallelization in HCPA.
In the example figure, there is one outer loop that contains two inner loops,
And each inner loop contains function calls.
In addition to hierarchically modeling the program execution,
HCPA also provides self-parallelism of each region,
which quantifies the amount of parallelism in each region.

## Slide 23: HCPA Step 2: Recursively Apply CPA
Total-Parallelism from
inner()
= ~7X
Total-Parallelism from
middle() and inner() = ~6X
Total-Parallelism from
outer(), middle(), and inner() = ~5X
What is a region’s parallelism
excluding the parallelism from its nested regions?

## Slide 24: HCPA: Introducing Self-Parallelism
a[i] = a[i] + 1;
b[i] = b[i] -1;
for (i=0 to 100) {
}
for (i=0 to 100) {
}
a[i] = a[i] + 1;
b[i] = b[i] -1;
2X
100X
200X
Total-Parallelism (from CPA)
Self-Parallelism
(from HCPA)
Represents a region’s ideal speedup
Differentiates a parent’s parallelism from its children’s
Analogous to self-time in serial profilers
Notes: ITALICIZE self-parallelism
So, what is self-parallelism?
To differentiate the parallelism metric used in CPA from self-parallelism,
I’ll call it total-parallelism.
As shown in the figure,
Total-parallelism represents the ideal speedup of the whole program.
In contrast, self-parallelism differentiates parent region’s parallelism from children’s and provides localized parallelism for each region.
In this example, the parallel loop’s self-parallelism is 100x
as parallelizing the loop will bring 100x speedup in ideal case.
Each iteration’s self-parallelism is two from instruction-level parallelism.
In this regard, self-parallelism is analoguous to self-time in serial profilers such as gprof.

## Slide 25: HCPA Step 3: Quantifying Self-Parallelism
for (i=0 to 100) {
}
a[i] = a[i] + 1;
b[i] = b[i] -1;
for (i=0 to 100) {
}
a[i] = a[i] + 1;
b[i] = b[i] -1;
a[i] = a[i] + 1;
b[i] = b[i] -1;
for (i=0 to 100) {
}
Self-Parallelism(Parent)
Total-Parallelism(Parent)
Total-Parallelism(Children)
Generalized Self-Parallelism Equation
Notes: HOW DO WE IMPLEMENT
Our intuition on quantifying self-parallelism is
The relationship between total-parallelism and self-parallelism.
As this figure indicates, conceptually, self-parallelism of the parent region can be computed
from total-parallelism of parent and children regions.
The challenge is to eliminate children region’s parallelism from Parent’s total-parallelism.
No, simple arithmetic divide does not work in general cases.
Now, let’s examine how Parkour quantifies self-parallelism.

## Slide 26: Self-Parallelism: Localizing Parallelism to a Region
Self-P (inner) = ~7.0 X
Self-P (middle) = ~1.0 X
Self-P (outer) = ~1.0 X
Notes: “the same”

## Slide 27: Classifying Parallelism Type
Leaf Region?
ILP
Loop Region?
P Bit == 1?
TLP
DOACROSS
DOALL
yes
no
no
yes
yes
no
See our paper for details…

## Slide 28: Why HCPA is an Even Better Thing
HCPA:
  Keeps all the desirable properties of CPA
  Localizes parallelism to a region via the self-parallelism metric and hierarchical region modeling
  Facilitates the classification of parallelism
  Enables more realistic modeling of parallel execution (see next slides)

## Slide 29: Outline
Introduction
  Background: Critical Path Analysis
  How Kismet Works
    HCPA
    Parallelization Planner
Experimental Results
Conclusion
Notes: 12:45
Now I’m going to talk about critical path analysis which Parkour extends,
and then show how parkour works with an example,
and then present the challenges in Parkour.
Let’s examine critical path analysis.

## Slide 30: Revisiting CPA Problem #2: Key Parallelization Constraints Are Ignored
Overhead
Exploitability
What type of parallelism is supported by the target platform?
e.g. Thread Level (TLP), Data Level (DLP), Instruction Level (ILP)
How many cores are available for parallelization?
Resource Constraints
Do overheads eclipse the benefit of the parallelism? e.g. scheduling, communication, synchronization
Notes: Revise title
“the key parallelization”
“the overhead”

## Slide 31: Parallelization Planner Overview
core count exploitability overhead …
Parallel
Execution Time Model
Planning Algorithm
Parallel
Speedup
Upperbound
Goal: Find the speedup upperbound based on the HCPA results and parallelization constraints.
Target-dependent
parallelization planner
region structure self-parallelism
HCPA profile
Constraints
Notes: Add one more input

## Slide 32: Planning Algorithm: Allocates Cores with Key Constraints
A sample core allocation process
for (j=0 to 32)
for (i=0 to 4)
for (k=0 to 2)
foo ();
bar1();
bar2();
loop i
self-p=4.0
loop j
self-p=32.0
loop k
self-p=1.5
foo()
self-p=1.5
bar1() self-p=2.0
bar2()
self-p=5.0
loop j
Max 4X
Max 32X
Max 2X
Exploitability
Core Count
Self-Parallelism
The allocated core count should not exceed ceil [self-p].
If a region’s parallelism is not exploitable, do not parallelize the region.
The product of allocated cores from the root to a leaf should not exceed the total available core count.
Max 5x
Max 2x
Max 2x
1X
1X
1X
The product should not exceed the available core count
Notes: Let’s examine Hierarchical Critical Path Analysis, or HCPA.
HCPA models the execution of a program with hierarchical regions,
Capturing hierarchical program structure such as loops and functions.
Each region works as a unit of parallelization in HCPA.
In the example figure, there is one outer loop that contains two inner loops,
And each inner loop contains function calls.
In addition to hierarchically modeling the program execution,
HCPA also provides self-parallelism of each region,
which quantifies the amount of parallelism in each region.

## Slide 33: Planning Algorithm: Finding the Best Core Allocation
core: 4X
core: 8X
core: 1X
Plan A
Plan B
Plan C
core: 2X
core: 4X
core: 4X
core: 2X
core: 16X
core: 16X
Highest Speedup
Core allocation plans for 32 cores
How can we evaluate the execution time for a specific core allocation?
Speedup
14.5X
Speedup 7.2X
Speedup
3.3X
Estimate the execution time for each plan and pick the one with the highest speedup.
Notes: “The planner”, “The planning algorithm” .. Note the article
Parallelization planner in Parkour determines the core allocation,
Incorporating parallelization constraints.
For example, this figure shows three different core allocations
And evaluate the estimated parallel execution time.
As the plan A brings the highest speedup, the planner selects plan A.
This exploration process is performed by planning algorithm.
As parallelization constraints are heavily target-dependent, we develop the planning algorithm for each platform with those constraints.
I will show two case studies of planning algorithm in the evaluation part.
Still there are a few target independent constraints in core allocation.
First, there is no need to allocate more cores than self-parallelism.
Also, if a region is not exploitable, then always allocate a single core.

## Slide 34: Parallel Execution Time Model: A Bottom-up Approach
loop i speedup=4.0
R is a non-leaf region
R is a leaf region
Bottom-up evaluation with each region’s estimated speedup and parallelization overhead O(R)
loop j speedup=4.0
loop k speedup=1.0
foo() speedup=1.0
bar1() speedup=1.0
bar2() speedup=1.0
ptime
(loop j)
ptime
(loop k)
ptime(loop i)
Notes: WHAT IS SPEEDUP?
When each region’s speedup is estimated,
Parkour can estimate the parallel execution time of the whole program,
Incorporating region-specific parallelization overhead O(R).
With hierarchical region model, the parallel execution time of a parent region is
affected by the parallel execution time of children regions. Considering this characteristics of hierarchical region model,
Parkour evaluates the parallel execution time of a program in a bottom-up fashion.
Thus, it starts evaluating the parallel execution time of leaf regions.
Since they don’t have children regions, the parallel execution time is estimated as
work divided by speedup added with parallelization overhead.
It then evaluates the execution time of loopj, loopk, and finally loop i –
eventually estimates the parallel execution time of the whole program.
And then parkour calculates the estimated speedup based on serial execution time.

## Slide 35: More Details in the Paper
How do we reduce the log file size of HCPA by orders of magnitude?
What is the impact of exploitability in speedup estimation?
How do we predict superlinear speedup?
And many others…

## Slide 36: Outline
Introduction
  Background: Critical Path Analysis
  How Kismet Works
Experimental Results
Conclusion
Notes: 12:45
Now I’m going to talk about critical path analysis which Parkour extends,
and then show how parkour works with an example,
and then present the challenges in Parkour.
Let’s examine critical path analysis.

## Slide 37: Methodology
Platform |  | 
Processor | 8 * Quad Core AMD Opteron 8380 | 16-core MIT Raw
Parallelization Method | OpenMP (Manual) | RawCC (Automatic)
Exploitable Parallelism | Loop-Level Parallelism (LLP) | Instruction-Level Parallelism (ILP)
Synchronization Overhead | High ( > 10,000 cycles) | Low ( < 100 cycles)
Compare estimated and measured speedup
To show Kismet’s wide applicability, we targeted two very different platforms
Raw
Multicore
Notes: Focus on “the multicore”
We compared Parkour estimated speedup against actual measured speedup.
To show Parkou’s wide applicability,
We target two very different platforms.
The first platform is Raw with 16-core MIT raw processor.
On Raw platform, an automatic parallelizing compiler called RawCC
Parallelizes code, exploiting instruction level parallelism with very low parallelization overhead.
The other platform is multicore with conventional AMD multicore processor.
On Multicore platform, we specifically target manual OpenMP parallelization
That exploits loop-level parallelism.
Unlike Raw, the parallelization cost on Multicore is quite high.

## Slide 38: Speedup Upperbound Predictions: NAS Parallel Benchmarks
Notes: Use a different color coding

## Slide 39: Speedup Upperbound Predictions: NAS Parallel Benchmarks
Predicting Superlinear Speedup
Without Cache Model
With Cache Model
Notes: Use a different color coding

## Slide 40: Speedup Upperbound Predictions: Low-Parallelism SpecInt Benchmarks
Notes: Reoder graphs in the order of our preference
Regenerate these graphs with y axis range (1 – 32)
Added linear speedup line (dotted)
Use color

## Slide 41: Conclusion
Kismet provides parallel speedup upperbound from serial source code.
HCPA profiles self-parallelism using a hierarchical
region model and the parallelization planner finds the best parallelization strategy.
Kismet will be available for public download in the first quarter of 2012.
We demonstrated Kismet’s ability to accurately
estimate parallel speedup on two different platforms.
Notes: Let me conclude this talk.

## Slide 42
***

## Slide 43: Self-Parallelism for Three Common Loop Types
DOACROSS
DOALL
CP
CP
CP
…
CP
CP
CP
…
(N/2) * CP
CP
Self- Parallelism
Loop Type
Loop’s
Critical Path
Length (cp)
N * CP
(N/2) * CP
= 2.0
N * CP
CP
= N
Work
N * CP
N * CP
CP
CP
CP
…
Serial
N * CP
N * CP
N * CP
= 1.0
N * CP
Notes: PUT SELF PARALLELISM NUMBERS IN RED
We have examined a DOALL loop example where all iterations are independent of each other,
but Parkour’s self-parallelism calculation works well for other loop types as well.
With a DOACROSS loop where half of the work in an iteration can overlap with the next iteration,
the critical path length of the loop is (N/2) * CP, and resulting self-parallelism is 2.0 which conforms to our intuition.
For a serial loop where the critical path length is identical to the adjusted work,
the calculated Self-parallelism is 1.0.
In all cases, Parkour successfully quantifies self-parallelism by extending CPA.

## Slide 44: Raw Platform: Target Instruction-Level Parallelism
Exploits ILP in each basic block by executing instructions on multiple cores
Leverages a low-latency inter-core network to enable fine-grained parallelization
Employs loop unrolling to increase ILP in a basic block
RawCC
Notes: 12:05
Let’s examine more about parallelization on Raw Platform.
Raw exploits instruction level parallelism in a basic block by executing instructions on different cores.
The left graph shows instruction dependence graph in a basic block –
Each instruction executes on different cores on the right,
as parallelized by RawCC.
This fine-grained parallelization is possible with Raw;ls low-latency inter-core netrwork.
Since the amount of ILP is typically limited,
Raw uses loop unrolling to increase the amount of ILP in a basic block.

## Slide 45: Adapting Kismet to Raw
Constraints to filter unprofitable patterns
  Target only leaf regions as they capture ILP
  Like RawCC, Kismet performs loop unrolling to increase ILP, possibly bringing superlinear speedup
Greedy Planning Algorithm
  Greedy algorithm works well as leaf regions will run independent of each other
  Parallelization overhead limits the optimal core count for each region
ILP
Non-ILP
A
B
C
D
E
F
16 Cores
8 Cores
16 Cores
Notes: 12:07
Now I’m going to talk how we adapted Parkour to Raw.
As we have discussed, Raw exploits ILP for parallelization.
Fortunately, ILP is captured in hierarchical region model with leaf regions.
Thus, Parkour set non-leaf regions as non-exploitable
and focuses on only leaf regions.
We use greedy planning algorithm to find the best core allocation
because each leaf region will be exclusively executed at a time.
Parkour finds the optimal number of cores based on parallelization cost and
Region’s work, and then estimates the parallel execution time of the whole program.

## Slide 46: Speedup Upperbound Predictions: Raw Benchmarks
Superlinear Speedup

## Slide 47: Multicore Platform: Target Loop-Level Parallelism
Models OpenMP parallelization focusing on loop-level parallelism
Disallows nested parallelization due to excessive synchronization overhead via shared memory
Models cache effect to incorporate increased cache size from multiple cores
Notes: 12:12
SHOULD we put AMD machine here?
Now let’s examine multicore platform.
Unlike Raw platform, Multicore platform focuses on loop-level parallelism.
We also disallows nested parallelization due to excessive synchronization cost in the platform.
As you can see in this figure, Multicore platform uses shared memory for synchronization,
and the cost is high in general.

## Slide 48: Adapting Kismet to Multicore
Solution (A) = {A:32} or {C:8, D:32}
Parallelize Descendants
Parallelize the Parent
Constraints to filter unprofitable OpenMP usage
  Target only loop-level parallelism
  Disallow nested parallelization
Bottom-up Dynamic Programming
  Parallelize either parent region or a set of descendants
  Save the best parallelization for a region R in Solution(R)
A
B
C
D
E
F
A
B
C
D
E
F
Parallelize
Don’t Parallelize
32 Cores
32 Cores
8 Cores
Notes: (NOTprofitable in OpenMP)
We adapted parkour to multicore with those constraints –
Target loop-level parallelism and disallow nested parallelization.
With these constraints, we developed a bottom-up dynamic programming algorithm.
First, we set non-loop regions as not exploitable.
Then, prohibiting nested parallelization brings an interesting property in parallelization planning.
You can either parallelize the parent region in a region hierarchy
or a set of descendant regions.
Parkour saves the best parallelization for each region R in Solution(R)
and propagates the solution to its parent.
In this example, Solution for B and D is parallelizing D with 32 cores,
And Solution for C, E, F is parallelizing C with 8 cores.
Combining these two solutions, Parkour estimates the parallel execution time
And compares it against the estimated parallel execution time when only parent region is parallelized.
In this manner, Parkour can find the best core allocation on the multicore platform.

## Slide 49: Impact of Memory System
Gather cache miss ratios for different cache sizes
Log load / store counts for each region
Integrate memory access time in time model